## Slide 1
Ant-Inspired Join/Leave Rule for BARI2D
Army-ant living-bridge feedback mapped onto BARI2D. Grey text: BARI2D observations and actions.
Potential joiners — free robots (not anchored)
Potential leavers — anchored robots
Walk on bank
or structure
follow beacon
FORWARD / turn
At the frontier?
Sense need
front / down IR: gap ahead
cue: robot ahead anchored
low
(frontier is further ahead)
high
(gap open right in front of me)
Cross, do not join
CLIMB onto the anchored robot,
FORWARD to its front end
Join
ANCHOR: grip the bank edge
or grip-and-extend
Be part of
structure
anchored to bank
or to a robot
Sense deficit
strain: load through my anchor
traffic: robots moving over me
large excess
(strain ≈ 0, no traffic for T steps)
deficit or needed
(load or traffic present)
Leave
RELEASE
Stay
keep the anchor (IDLE)
reduces deficit — remaining gap to span, missing load capacity
reduces excess — idle, redundant grips
Notes: Free robots walk toward the gap. At the frontier they sense whether a new link is needed: if the gap is open right in front of them they join (ANCHOR at the bank edge or grip-and-extend); if the frontier is further ahead they cross (CLIMB, walk to the front end). Anchored robots sense the deficit through the load on their anchor (strain) and traffic over them. If neither is present for T steps they leave (RELEASE); otherwise they stay. Joining reduces the deficit (remaining gap, missing load capacity); leaving reduces the excess (redundant grips such as the side-by-side edge grips seen in v3).

## Slide 2
Mapping the Rule onto BARI2D
Each decision uses only local sensing; each outcome is one discrete action.
Army-ant rule | BARI2D local sensing | BARI2D action
Walk on trail | beacon, IR | FORWARD / turn
Sense bridge performance | front / down IR: gap ahead; cue: robot ahead anchored | —
Not very high → cross | frontier is further ahead | CLIMB, FORWARD to front end
Very high → join | gap open right in front of me | ANCHOR (bank edge / grip-and-extend)
Sense deficit | strain through my anchor; traffic over me | —
Large excess → leave | strain ≈ 0 and no traffic for T steps | RELEASE
Otherwise → stay | load or traffic present | keep anchor (IDLE)
Deficit — joining reduces it
Remaining gap to span: front end → far bank (1 − span progress)
Missing load capacity: max(0, target load − LP max load)
Excess — leaving reduces it
Anchored robots carrying no load and no traffic
e.g. side-by-side edge grips seen in v3
Status in the code
Available: IR, strain, structure cues (v4), ANCHOR / RELEASE / CLIMB
Traffic: auxiliary target only, not a direct input
T-step persistence: GRU memory or an explicit counter